## Slide 1: CSCI 3302 Introduction to Robotics
Alessandro Roncone
aroncone@colorado.edu

## Slide 2
Lab 5 Mapping and Planning

## Slide 3: Recap
Lab 2 – Forward Kinematics [wheel velocities → robot x, y, θ]
Lab 3 – Inverse Kinematics + Feedback Control
Lab 4 – Mapping
Lab 5 [today – April 7] -- Put it all together

## Slide 4: Today: Odometry, Mapping and Inverse Kinematics
???
How can I put it all together?
X
Y
rotation
???
???
Notes: Photoresistor decreases resistance with increasing incident light intensity

## Slide 5: Lab Setup
240° range
First 83 + last 83 rays thrown away due to hardware design
TIAGo
Notes: Photoresistor decreases resistance with increasing incident light intensity

## Slide 6: What problems did you run into when using the laser sensor map?

## Slide 7
Noise. Obstacles everywhere!
Sources: reflections, artifacts from robot braking, etc.
Turn measurements (true/false) into a probability
Grid map stores the probability of a cell being an obstacle or not
Every positive measurement increases the probability
Use a threshold to decide

## Slide 8: What problems did you run into when programming a path-following system?

## Slide 9: Control issues
Find the right trade-offs in your gains
Minimize settling time
Minimize tracking error
Learn to live with your controller not being perfect and stay away from obstacles

## Slide 10: What parameter do you think will affect planning time the most?

## Slide 11
C-SPACE

## Slide 12: Path Planning
Dijkstra's
A*

## Slide 13: 3 modes in provided code skeleton
Manual mode for mapping
    Use keyboard control to drive around
    Save generated map to map.npy
Planner mode for path generation
    Implement + test planning algorithm on toy map (to parallelize teamwork)
    Create configuration space. Visualize.
    Plan path (using A*[highly recommended] or Dijkstra's) in config space. Save planned path to .npy file.
Autonomous mode for path following
    Load path from .npy file. Visualize.
    Execute using feedback control

## Slide 14: This lab is worth 150 points!
FAQs:
What’s due at the end of today?
  Nothing, this is a 2.5-week lab. Due Friday 04/07 at 11:59pm.
What do I turn in?
  ONE person needs to turn in the lab report and code per group.
We’re done! Can we leave?
  Yep. Lab is meant to provide an interactive problem-solving time. If you complete the work early, you are free to go!

## Slide 15: Questions?